## Slide 1: ECE/CS 552: Pipelining and Exceptions
© Prof. Mikko Lipasti
Lecture notes based in part on slides created by Mark Hill, David Wood, Guri Sohi, John Shen and Jim Smith

## Slide 2: Exceptions
What happens?
  Instruction fetch page fault
  Illegal opcode
  Privileged opcode
  Arithmetic overflow
  Data page fault
  I/O device status change
  Power-on/reset

## Slide 3: Exceptions
For some, we could test for the condition
  Arithmetic overflow
  I/O device ready (polling)
But most tests uselessly say “no”
Solution:
  Surprise “procedure call”
  Called an exception

## Slide 4: Exceptions: Big Picture
Two types:
  Interrupt (asynchronous) or
  Trap (synchronous)
Hardware handles initial reaction
Then invokes a software exception handler
  By convention, at e.g. 0xC00
  O/S kernel provides code at the handler address

## Slide 5: Exceptions: Hardware
Sets state that identifies cause of exception
  MIPS: in exception_code field of Cause register
Changes to kernel mode for dangerous work ahead
Disables interrupts
  MIPS: recorded in status register
Saves current PC (MIPS: exception PC)
Jumps to specific address (MIPS: 0x80000080)
  Like a surprise JAL – so can’t clobber $31

## Slide 6: Exceptions: Software
Exception handler:
  MIPS: .ktext at 0x80000080
Set flag to detect incorrect entry
  Nested exception while in handler
Save some registers
Find exception type
  E.g. I/O interrupt or syscall
Jump to specific exception handler

## Slide 7: Exceptions: Software, cont’d
Handle specific exception
Jump to clean-up to resume user program
Restore registers
Reset flag that detects incorrect entry
Atomically
  Restore previous mode (user vs. supervisor)
  Enable interrupts
  Jump back to program (using EPC)

## Slide 8: Implementing Exceptions
We worry only about hardware, not s/w
IntCause
  0 undefined instruction
  1 arithmetic overflow
Changes to the datapath
  Detect exception
  Additional source for next PC
  Storage for exception cause, return address, spare register
Additional complexity in control logic

## Slide 9: Pipeline With Exceptions (Fig 4.66)

## Slide 10: Summary and Review
Exceptions
Handling exceptions in a pipelined design